## Slide 1: BLUETOOTH low energy (BLE)
Final project - Carlos estay
ANDROID DEVELOPMENT – dmit2504

## Slide 2: Project objective
Build an android app to remotely control a 4 wheel robot using BLE
Control speed using slider (SeekBar)
Control 4 possible moves with 4 buttons:
  Forward
  Reverse
  Turn right
  Turn left

## Slide 3: Project objective
Components to use:
  Android Phone
  Custom modified robot
  Microcontroller module: NUCLEO-L476RG
    https://www.st.com/en/evaluation-tools/nucleo-l476rg.html
  BLE module: X-NUCLEO-IDB05A1
    https://www.st.com/en/ecosystems/x-nucleo-idb05a1.html

## Slide 4: Interaction diagram
https://www.dimensionengineering.com/appnotes/simple_robot/

## Slide 5: basic control of a 4 wheel robot
https://www.servomagazine.com/magazine/article/may2014_McComb

## Slide 6: Pulse width modulation (PWM)
https://www.analogictips.com/pulse-width-modulation-pwm/

## Slide 7: BLE characteristics
Transmits small amounts of data between devices
It is designed for low power consumption
Normally used for:
  Proximity sensors
  Heart rate monitors
  Fitness devices
  Remote control

## Slide 8: BLE ACTORS
GATT : Generic Attribute Profile
GATT Server
GATT Client
Services: unique UUID identifier
Characteristics: a service can have many characteristics. Also identified by a UUID

## Slide 9: BLE ACTORS EXAMPLE
GATT SERVER
SERVICE
SERVICE
CHARACTERISTIC
CHARACTERISTIC
CHARACTERISTIC
CHARACTERISTIC
CHARACTERISTIC
CHARACTERISTIC
GATT CLIENT

## Slide 10: STEPS TO CONNECT TO A GATT SERVER
STEP 1: enable permissions in android manifest
<uses-permission android:name="android.permission.BLUETOOTH_ADMIN" /> <uses-permission android:name="android.permission.BLUETOOTH" /> <uses-permission android:name="android.permission.ACCESS_COARSE_LOCATION" />

## Slide 11: STEPS TO CONNECT TO A GATT SERVER
STEP 2: Request for permission in run time, if not yet enabled
//Check and request permission if necessary if (ContextCompat.checkSelfPermission(this, Manifest.permission.ACCESS_COARSE_LOCATION) != PackageManager.PERMISSION_GRANTED) { // Permission is not granted if (ActivityCompat.shouldShowRequestPermissionRationale(this, Manifest.permission.ACCESS_COARSE_LOCATION)) { } else { // No explanation needed; request the permission ActivityCompat.requestPermissions(this, new String[]{Manifest.permission.ACCESS_COARSE_LOCATION}, 1); // result of the request. } } else { // Permission has already been granted }

## Slide 12: STEPS TO CONNECT TO A GATT SERVER
Classes to utilize to scan devices and to connect
  BluetoothManager
  BluetoothAdapter
  BluetoothGattServer : if you are setting device as a server
  BluetoothGatt
  BluetoothGattCharacteristic
  BluetoothDevice
  BluetoothLeScanner
  Handler: to handle the Scan function

## Slide 13: STEPS TO CONNECT TO A GATT SERVER
STEP 3: initialize the Bluetooth adapter
//Initialize Bluetooth adapter bluetoothManager = (BluetoothManager) getSystemService(Context.BLUETOOTH_SERVICE); bluetoothAdapter = bluetoothManager.getAdapter();
//Enable Bluetooth if not yet enabled if(bluetoothAdapter == null || !bluetoothAdapter.isEnabled()){ Intent enableBtIntent = new Intent(BluetoothAdapter.ACTION_REQUEST_ENABLE); startActivityForResult(enableBtIntent, REQUEST_ENABLE_BT); }

## Slide 14: STEPS TO CONNECT TO A GATT SERVER
STEP 4: Scan for devices – call scanLeDevice() function (or any name)
@TargetApi(21) private void scanLeDevice(final boolean enable) { final BluetoothLeScanner bluetoothLeScanner = bluetoothAdapter.getBluetoothLeScanner(); if (enable) { statusTextView.setText("Scanning..."); // Stops scanning after a pre-defined scan period. handler.postDelayed(new Runnable() { @Override public void run() { mScanning = false; bluetoothLeScanner.stopScan(leScanCallback); statusTextView.setText("Scan stopped"); } }, SCAN_PERIOD); mScanning = true; bluetoothLeScanner.startScan(leScanCallback); } else { mScanning = false; bluetoothLeScanner.stopScan(leScanCallback); } }

## Slide 15: STEPS TO CONNECT TO A GATT SERVER
STEP 4: Scan for devices – Handle callback

## Slide 16: STEPS TO CONNECT TO A GATT SERVER
STEP 4: Scan for devices – Handle results
  The result.getDevice() will return the Bluetooth Device to connect to.
    BluetoothDevice myDevice = result.getDevice();
    String myDeviceName = myDevice.getName;
    String myDeviceAddress = myDevice.getAddress;

## Slide 17: STEPS TO CONNECT TO A GATT SERVER
STEP 4: Scan for devices – Handle results

## Slide 18: STEPS TO CONNECT TO A GATT SERVER
STEP 5: Select a device and connect to the Gatt server
  myDevice.connectGatt(thisActivity, false, gattCallback);

## Slide 19: STEPS TO CONNECT TO A GATT SERVER
STEP 6: Handle gattCallback results

## Slide 20: STEPS TO CONNECT TO A GATT SERVER
STEP 6: Handle gattCallback results - Discover services if connected
@Override public void onConnectionStateChange(BluetoothGatt gatt, int status, int newState) { //super.onConnectionStateChange(gatt, status, newState); connectedDevice = gatt.getDevice(); switch(newState ){ case BluetoothProfile.STATE_CONNECTED: bluetoothGatt.discoverServices(); break; case BluetoothProfile.STATE_DISCONNECTED: break; default: break; }

## Slide 21: STEPS TO CONNECT TO A GATT SERVER
STEP 7: Get service and characteristic to use
@Override public void onServicesDiscovered(BluetoothGatt gatt, int status) { //super.onServicesDiscovered(gatt, status); List<BluetoothGattService> services = gatt.getServices(); String serviceUUID = "D973f2E0-B19E-11E2-9E96-0800200C9A66"; String charUUID = "D973f2E2-B19E-11E2-9E96-0800200C9A66"; BluetoothGattService service = gatt.getService(UUID.fromString(serviceUUID)); customCharacteristic = service.getCharacteristic(UUID.fromString(charUUID)); }

## Slide 22: STEPS TO CONNECT TO A GATT SERVER
STEP 8: Write into custom characteristic
customCharacteristic.setValue("@MF0"); bluetoothGatt.writeCharacteristic(customCharacteristic);
//Robot connected, open remote control activity Intent intent = new Intent(getApplicationContext(), RemoteControlActivity.class); intent.putExtra("ROBOT", robotDevice); startActivity(intent);
Pass Bluetooth device to a different activity if desired

## Slide 23: COMMANDS IMPLEMENTED FOR ROBOT
“@MF0” : Move Forward
“@MB0” : Move Reverse
“@MR0” : Turn Right
“@ML0” : Turn Left
“@SXX” : Set speed to XX-> from 00 to 10

## Slide 24: SUMMARY OF STEPS
Enable permissions in android manifest
Request permission ACCESS_COARSE_LOCATION in run time
Initialize Bluetooth Adapter
Scan devices: bluetoothLeScanner.startScan(leScanCallback);
  Declare and handle (leScanCallback)
  If onScanResult is called, add result to a list view
  Once a result (device) is selected, go to step 5

## Slide 25: SUMMARY OF STEPS
5. Connect to Gatt Server: myDevice.connectGatt(thisActivity, false, gattCallback);
6. Declare and handle gattCallback
  if onConnectionStateChange is called and new state is STATE_CONNECTED, go to step 7
7. Get service and characteristic
  If onServiceDiscovered is called, get desired service, if discovered, and characteristic
8. Write to custom characteristic selected
  onCharacteristicWrite will be called as an acknowledge that the characteristic was written properly.

## Slide 26: POSSIBLE OTHER IMPLEMENTATIONS OF BLE
Create a Bluetooth Chat between 2 android devices, one configured as a Gatt Client and other one as a Gatt Server
Create a chat between an android device and a computer that as a microcontroller with BLE module, which outputs the messages received in a terminal such as Tera Term, for instance
Read other standard BLE devices/profiles. For instance, a heart rate monitor
Use the android device as an extra or custom controller for a game

## Slide 27: Contact details - questions
carlos.estayo@gmail.com
cestayoyarzo1@studentmail.nait.ca